## Slide 1
DC INTERFERENCE
CHARLIE POORE
NACE SENIOR CORROSION TECHNOLGIST #53904

## Slide 2
Detection and Confirmation
Mitigation and Monitoring
Part 1

## Slide 3: Poll: IS “DC Interference” coming up in your pipeline integrity or corrosion meetings?
Every single day
We talk about it quite a bit
I’ve heard the term before
Never heard of it

## Slide 4: Cathodic Protection in General Terms is….
+ Potential -
Location (MP)
Native Potential
Polarized Potential
Application of DC current to the exterior of the pipeline to electrochemically inhibit naturally occurring corrosion.

## Slide 5: INTERFERENCE
Hear the word Interference we typically think AC Interference-buzzword last 10 years
Definition of interference-”the action of interfering or the process of being interfered with”
Definition of Interfere-”take part or intervene in an activity without invitation or necessity or to prevent a process or activity from continuing or being carried out properly.

## Slide 6: INFLUENCE
The capacity to have an effect on the character, development, or behavior of someone or something, or the effect itself

## Slide 7: DC INTERFERENCE is Any Adverse Effect on The Electrical Potentials of a Buried or Submerged Structure
Not To Be Confused With:
STRAY CURRENT
Current traveling through any un-intended path. May cause STRAY CURRENT CORROSION.
INFLUENCE
Change in a structure to electrolyte potential reading, but not necessarily the structure
Impacts Buried Structures such as …
  Pipelines
  Well Casings
  Metal Fences
  Electrical Transmission
  Distribution Equipment
  Telephone Equipment
  Electrical Grounding Equipment
  Residential Copper Plumbing
  Residential Propane Piping

## Slide 8: The consequences can be:
Inaccurate Cathodic Protection Potential Readings
Ineffective Cathodic Protection
Stray Current Corrosion

## Slide 9
Stray Current Corrosion Carbon Steel Example…Faradays Law
If 10 mA discharging for 1 year, then..
W = .20#
W = (20#/A-Yr)
(0.01A)
(1 Yr)

## Slide 10: DC INTERFERENCE can be…
STATIC
  Relatively Constant Magnitude
  Follows Same Geographic Path
  Examples:
    CATHODIC PROTECTION SYSTEMS
    HIGH VOLTAGE DC SYSTEMS
    LARGE SCALE DC WELDING
DYNAMIC
  Fluctuating in Magnitude and Direction
  Can Change Geographic Path
  Examples
    DC TRANSIT SYSTEMS-lose DC leg-earth becomes return
    LARGE SCALE DC WELDING
    TELLURIC CURRENTS
NATURALLY OCCURING STRAY CURRENTS CAUSED BY DISRUPTIONS IN EARTH’S MAGNECTIC FIELD FROM SUNSPOT ACTIVITY.

## Slide 11: Detection of DC Interference-NACE/AMPP SPO 169 Standard
During external corrosion control surveys, personnel should be alert for electrical or physical observations that could indicate interference from a foreign source such as the following:
9.3.1.1 Pipe-to-electrolyte potential changes or fluctuations on the affected structure caused by a foreign source;
9.3.1.2 Changes or fluctuations in the line current magnitude or direction caused by a foreign source;
9.3.1.3 Localized pitting in areas near or immediately adjacent to a foreign structure
9.3.1.4 Damage to external coatings in a localized area near an anode bed or near any other source of stray current.

## Slide 12: Early Warning Signs...
+ Potential -
Location (MP)
Native Potential
Polarized Potential
“Low Potentials vs. surrounding area or vs. previous survey.
Changes in CP Current Magnitude and Direction
Severe Pitting Corrosion

## Slide 13: The Usual Suspects
1. “Low” or Positive CIS potentials near foreign crossing.
2. Potentials more negative than expected near a foreign current source.
3. Significant corrosion damage uncovered during an ILI validation dig or ECDA dig.

## Slide 14
ANODIC or CATHODIC INTERFERENCE?
or
EARTH VOLTAGE GRADIENT?
Pipe-to-soil potential measurement
  Abnormally ‘high’ or more electro-negative
  Abnormally ‘low’ potential or more electro-positive
Field Investigation

## Slide 15
EVG
Ground Gradient
Anode Influence
IR Drop
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
All DC current will create an EVG
EVG does not, by itself, indicate the presence of DC interference
+
V=IR where:
V = Voltage Gradient
I = Current
R = Passing Through Earth Resistance
DC INTERFERENCE vs. Earth Voltage Gradient… OHM’s Law

## Slide 16
Cathodic Gradient
Pipelines and Protected Structures
Earth Voltage Gradient
Anodic Gradient
CP Ground beds
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.

## Slide 17
BARE PIPE
Cathodic Effects can be widespread
COATED PIPE
~95% of the EVG is within 10 diameters of the holiday
Bare
Coated Pipe
Earth Voltage Gradient

## Slide 18
A location on the earth far enough away from the affected structure that the earth potential gradients associated with current flowing in the earth to/from the affected structure are insignificant
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
Understanding Remote Earth

## Slide 19
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
Cathodic Interference
Foreign pipeline passing through intense Cathode gradients
Overlapping EVG is more NEGATIVE than remote earth
Notes: Gradients on a cathode will attract positive current toward the surface of the protected pipeline.

## Slide 20
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
PIPE-TO-SOIL POTENTIAL READINGS ARE MORE POSITIVE NEAR THE POINT OF CROSSING IN A CATHODIC GRADIENT
HOWEVER, THERE MAY BE NO ACTUAL CURRENT DISCHARGING
Cathodic Interference

## Slide 21
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
Foreign pipeline passing through intense Anode gradients
Overlapping EVG is more POSITIVE than remote earth
Anodic Interference

## Slide 22
Image source(s):
*Peabody, A. W., and Ronald L. Bianchetti. Peabody’s Control of Pipeline Corrosion, TX: NACE International, the Corrosion Society, 2001.
Anodic Interference
PIPE-TO-SOIL POTENTIAL READINGS ARE MORE NEGATIVE NEAR THE POINT OF CROSSING IN AN ANODIC GRADIENT
HOWEVER, THERE MAY BE NO ACTUAL CURRENT COLLECTING

## Slide 23: Poll: Did you How would you rate your own knowledge of DC Interference?
This is way over my head
I have a few questions
I know DC interference pretty well
I should be teaching this webinar

## Slide 24: Potential Testing Techniques
DC Interference

## Slide 25
Reference cell placement
Soil conditions
Structure depth
Coating condition…bare?
Foreign Structure anodic or cathodic gradients
EVG gradients due to ICCP or galvanic anodes
Consider…

## Slide 26
Identify source of stray DC current
Interrupt suspected source(s)
  Use caution here…must be able to verify each source contribution
Conduct transverse P/S potential measurements
and /or
Conduct transverse EVG measurements
Conduct limited CIS to define boundaries of influence
Measure Polarization Waveform
Investigate...

## Slide 27
NORMAL OPERATING CONDITION INDICATED
UTILIZES SINGLE REFERENCE CELL
HIGH INPUT IMPEDANCE MULTIMETER
STRUCTURE CONTACT
REMOTE P/S READINGS ARE NORMALLY MORE NEGATIVE THAN CLOSE READINGS
Transverse P/S potential measurement

## Slide 28
UTILIZES TWO BALANCED REFERENCE CELLS
Transverse P/S potential measurement
HIGH INPUT IMPEDANCE DIGITAL MULTIMETER
THIS IS NOT A P/S MEASUREMENT
ALL MEASUREMENTS MUST INCLUDE ACCURATE RECORDING OF VOLTAGE MAGNITUDE AND POLARITY WITH REFERENCE TO PIPE
CURRENT PICKUP BY STRUCTURE

## Slide 29: Polarization Wave Form Analysis
Use Data Logger or Field Data Computer
Select “Graph”
Set timeframe to match interruption cycle
Adjust graph limits to show entire wave form

## Slide 30
Chart: Interruption Group
Location #1
Polarization from source #1 (Local)
Serious influence from group #2 (Foreign)
No Depolarization from group #2, not “Picking up” on pipeline. Reference Cell is likely within EVG.
Need to interrupt Group #2 during annual
Operator “Off”
Polarization Wave Form Analysis

## Slide 31
Chart: Interruption Group
Location #2
Location where damage was found previously
Almost zero influence from Operator CP source
Note IR change and re-polarization when Foreign group 2 is off
Foreign “Off”

## Slide 32: Current Testing Techniques
DC Interference

## Slide 33
Current Testing for DC Interference
YOUR PIPELINE
Foreign Pipeline
Gradient Area of Influence

## Slide 34
4-wire Test Station
YOUR PIPELINE
x
x - i
i

## Slide 35
Current Mapping
YOUR PIPELINE
S
S - i
i

## Slide 36
Coupon Test Station
YOUR PIPELINE
Measure potentials at depth
Measure Current Magnitude and Direction

## Slide 37
In-Line Inspection
YOUR PIPELINE

## Slide 38
Clamp-on Meter
YOUR PIPELINE

## Slide 39
Additional Test Procedures
YOUR PIPELINE
INLINE INSPECTION
4-WIRE TEST STATION
COUPON TEST STATION
CLAMP-ON METER
CURRENT MAPPING

## Slide 40: Poll: Which of these technologies or techniques are you already familiar with?
Select All That Apply
Coupon Test Stations
Four-Wire Current Measurement Test Stations
Depolarization Testing
Current Measurement via Inline Inspection

## Slide 41: SUMMARY
Understand earth voltage gradient (EVG) effects
Understand anodic/cathodic interference characteristics
Understand available tools, testing techniques & data interpretation
  Polarization Measurement
  Transverse P/S potential measurement
  Transverse EVG measurement
  4 wire test station
  Current mapping
  ILI
  Clamp-on ammeter
  Coupon test station

## Slide 42
Detection and Confirmation
Mitigation and Monitoring

Part 2

## Slide 43: Poll: Which of these describes your company?
We’ve got a good handle on DC interference ourselves
We’ve got an expert we call on when needed
We need some help figuring out where to start

## Slide 44: What We Established in Part 1…
+ Potential -
Location (MP)
Potential
Our pipeline is picking up stray current from somewhere.
Possibly a foreign pipeline CP system

## Slide 45: What We Established in Part 1…
+ Potential -
Location (MP)
Potential
Our pipeline is picking up stray current from somewhere.
Possibly a metallic connection or bond

## Slide 46: What We Established in Part 1…
+ Potential -
Location (MP)
Potential
Our pipeline is picking up stray current from somewhere.
Possibly from DC transit or another DC source

## Slide 47: What We Established in Part 1…
+ Potential -
Location (MP)
Potential
Our pipeline is giving back stray current somewhere.
This is where the corrosion issue occurs

## Slide 48: Simple Mitigation Techniques
DC INTERFERENCE

## Slide 49: Mitigating Anodic Interference
Location (MP)
Turn Down the Foreign CP System
Not always practical
Easy for foreign operator to reverse without notice

## Slide 50: Mitigating Anodic Interference
Location (MP)
Install a “Current Collection” System
Negatively affects foreign operator CP system

## Slide 51: Mitigating Anodic Interference
Location (MP)
Relocate the Foreign CP System
Expensive but permanent
May be easement issues, consider deep anode beds

## Slide 52: Mitigating Anodic Interference
Location (MP)
Re-Coat Our Pipeline in the Pickup Area
Expensive
Not a guaranteed fix, requires eliminating all coating holidays in the area

## Slide 53: Mitigating Cathodic Interference
Location (MP)
Turn Down the Foreign CP System
Shrinks the Cathodic Gradient
Not always practical
Easy for foreign operator to reverse without notice

## Slide 54: Mitigating Cathodic Interference
Location (MP)
Install “Current Discharge” Anodes
Moves the current discharge point
Practical and inexpensive
Requires monitoring and eventual replacement of anodes

## Slide 55: Mitigating Cathodic Interference
Location (MP)
Increase our Cathodic Protection Current
“Push back” on foreign DC influence
Easy to do with well coated line
Requires monitoring

## Slide 56: Mitigating Cathodic Interference
Location (MP)
Recoat Foreign Line in Interference Area
Reduce foreign CP gradient in the area
Expensive and hard to explain sometimes

## Slide 57: Mitigating Cathodic Interference
Location (MP)
Bond to the Foreign CP System
Last Resort
Ties your CP systems together
Creates a “critical bond” that must be monitored on regulated pipeline

## Slide 58: Poll: Which mitigation approach is your typical go-to today?
Just bond it!
Field test first and see if it’s really interference.
Just leave it, you’re retiring soon anyway.

## Slide 59: Monitoring the situation
DC INTERFERENCE

## Slide 60
Monitoring is naturally incorporated into annual potential surveys.
Key Locations:
Near Foreign CP Systems
At Foreign Pipeline Crossings
Near DC Transit/Other Sources
Monitoring Potentials

## Slide 61: Monitoring Potentials
My Pipeline
+ Potential (mV) -
Location (MP)
Test station placement is critical in avoiding foreign cathodic gradients
Stationary reference cells at depth should be considered for accurate readings

## Slide 62: Using Coupon Test Stations
Coupon simulates a coating defect
  On
    Coupon is connected to the structure being protected.
  Instant Off
    Coupon can quickly be disconnected from the structure, eliminating ALL current sources affecting the protected structure.
  Native State
    A second coupon that is NEVER connected to the structure, giving it a true native state potential.
DC Current Density
  Known coupon size allows for quick current measurement (Assuming you can disconnect the coupon)
100 cm2 DC Native Coupon
100 cm2 DC
Test Coupon
Reference Electrode

## Slide 63: Monitoring Potentials AND Current
Stationary reference cells and coupon test stations allow for the use of data loggers and remote monitors.
Data collection over time is the key to detecting transient or dynamic DC interference
Remote monitors with level-set alarms can be used to detect and respond to DC interference quickly

## Slide 64: QUESTIONS?
CHARLIE POORE
NACE/AMPP Senior Corrosion Technologist #53904
charlie.poore@mesaproducts.com
505-250-7481